## Slide 1
Computer Networking: A Top-Down Approach 8th Edition, Global Edition Jim Kurose, Keith Ross Copyright © 2022 Pearson Education Ltd
Chapter 5 Network Layer: Control Plane
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Adapted by renping.liu@uts.edu.au on 30 April 2023
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
Re-do of network management slides; redo of Bellman-Ford slides

## Slide 2: Making routing scalable
our routing study thus far - idealized
all routers identical
network “flat” – abstracted Graph
… not true in practice
scale: billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy:
Internet: a network of networks
each network admin may want to control routing in its own network

## Slide 3: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
intra-AS (aka “intra-domain”): routing among within same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocols
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es
inter-AS (aka “inter-domain”): routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)
Countries in the World

## Slide 4: Network layer: “control plane” roadmap
5.1 introduction
5.2 routing protocols
5.3 intra-ISP routing: OSPF
5.4 routing among ISPs: BGP
5.5 SDN control plane
5.6 Internet Control Message Protocol
5.7 network management, configuration

## Slide 5: Intra-AS routing: routing within an AS
most common intra-AS routing protocols:
RIP: Routing Information Protocol [RFC 1723]
  classic DV: DVs exchanged every 30 secs
  no longer widely used
EIGRP: Enhanced Interior Gateway Routing Protocol
  DV based
  formerly Cisco-proprietary for decades (became open in 2013 [RFC 7868])
OSPF: Open Shortest Path First [RFC 2328]
  link-state routing
  IS-IS protocol (ISO standard, not RFC standard) essentially same as OSPF

## Slide 6: OSPF (Open Shortest Path First) routing
“open”: publicly available
classic link-state
  each router floods OSPF link-state advertisements (directly over IP rather than using TCP/UDP) to all other routers in entire AS
  multiple link costs metrics possible: bandwidth, delay
  each router has full topology, uses Dijkstra’s algorithm to compute forwarding table
security: all OSPF messages authenticated (to prevent malicious intrusion)
OSPF

## Slide 7: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements flooded only in area, or backbone
  each node has detailed area topology; only knows direction to reach other destinations
area border routers: “summarize” distances to destinations in own area, advertise in backbone
area 1
area 2
area 3
Backbone
Area 0
internal
routers
backbone router: runs OSPF limited to backbone
boundary router: connects to other ASes
local routers:
flood LS in area only
compute routing within area
forward packets to outside via area border router

## Slide 8: Network layer: “control plane” roadmap
5.1 introduction
5.2 routing protocols
5.3 intra-ISP routing: OSPF
5.4 routing among ISPs: BGP
5.5 SDN control plane
5.6 Internet Control Message Protocol
5.7 network management, configuration

## Slide 9: Inter-AS routing: a role in intradomain forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
suppose router 1a in AS1 receives datagram destined outside of AS1 (e.g., AS6):
AS1 inter-domain routing must:
learn which destinations reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
  router should forward packet to gateway router in AS1, but which one?
AS6

## Slide 10: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
allows subnet to advertise its existence, and the destinations it can reach, to rest of Internet: “I am here, here is who I can reach, and how”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy

## Slide 11: eBGP, iBGP connections
eBGP connectivity
logical iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols

## Slide 12: BGP basics
when AS3 gateway 3a advertises path AS3,X to AS2 gateway 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
BGP advertisement:
AS3, X

## Slide 13: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
AS3, X

## Slide 14: Path attributes and BGP routes
BGP advertised route: attributes, prefix
  prefix: destination being advertised
  two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes
AS1’s BGP route to X:
AS2,AS3,X
- prefix=X
- AS-PATH: AS2,AS3
- NEXT-HOP: AS2

## Slide 15: BGP path advertisement (more)
AS2,AS3,X
AS1 gateway router 1c learns path AS2,AS3,X from 2a
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
based on policy, AS1 gateway router 1c chooses path AS3,X and advertises path within AS1 via iBGP
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS3,X
AS3,X
AS3,X

## Slide 16: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 17: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
forwarding
table
forwarding table configured by intra- and inter-AS routing algorithms
Intra-AS
Routing
Inter-AS
Routing
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 18: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS2,AS3,X
AS3,X
AS3, X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
1
2
dest
interface
…
…
…
…
local link interfaces
at 1a, 1d
at 1d: to get to X, use interface 1
1c
1
X
1
AS3,X
AS3,X
AS3,X

## Slide 19: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
at 1d: to get to X, use interface 1
dest
interface
…
…
…
…
1c
2
X
2
at 1a: OSPF intra-domain routing: to get to 1c, use interface 2
at 1a: to get to X, use interface 2

## Slide 20: Mid-break
  ☕️
Q&A

## Slide 21: Why different Intra-, Inter-AS routing ?
performance:
intra-AS: can focus on performance
inter-AS: policy dominates over performance
policy:
intra-AS: single admin, so policy less of an issue
inter-AS: admin wants control over how its traffic routed, who routes through its network
scale:
hierarchical routing saves table size, reduced update traffic
Diplomacy

## Slide 22: Hot potato routing
2c
2d
2b
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
2d learns (via iBGP) it can route to X via 2a or 2b
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a - not 2b!, even though more AS hops to X): don’t worry about inter-domain cost!
AS3,X
AS1,AS3,X
OSPF link weights
201
112
263
2b or not 2b?
Conflict of Interest
between Inter/Intra-

## Slide 23: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 24: BGP: advertising policy – ISP case
B,A,w
B
legend:
customer
network:
provider
network
A advertises path Aw to B and to C
B advertises path B,A,w to x, C advertises C,A,w to x and y
B chooses not to advertise B,A,w to C!
  B gets no “revenue” for routing C,B,A,w, since none of y or w are B’s customers
  C does not learn about C,B,A,w path
C will route C,Amw (not using B) to get to w
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,w
A,w
B,A,w
C,A,w
C,A,w
✘

## Slide 25: BGP: advertising policy – enterprise case
Customer x is dual-homed: attached to two networks
  x receives path to y (Cy) from C
  if x advertise C to B,
  then BCy traffic could go through x - NOT x’s responsibility (not an ISP!).
policy to enforce: x does not want to route from B to C via x
  .. so x will not advertise to B a route to C
  As a result, x will not carry BCy traffic
A
B
C
W
X
Y
legend:
customer
network:
provider
network
✘
xCy
Cy
✘

## Slide 26: Network layer: “control plane” roadmap
5.1 introduction
5.2 routing protocols
5.3 intra-ISP routing: OSPF
5.4 routing among ISPs: BGP
5.5 SDN control plane
5.6 Internet Control Message Protocol
5.7 network management, configuration

## Slide 27: ICMP: internet control message protocol
used by hosts and routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP messages carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 28: Traceroute and ICMP
when ICMP message arrives at source: record RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes
source sends sets of UDP segments to destination
  1st set has TTL =1, 2nd set has TTL=2, etc.
datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message possibly includes name of router & IP address

## Slide 29: Network layer: “control plane” roadmap
5.1 introduction
5.2 routing protocols
5.3 intra-ISP routing: OSPF
5.4 routing among ISPs: BGP
5.5 SDN control plane
5.6 Internet Control Message Protocol
5.7 network management, configuration

## Slide 30: What is network management?
autonomous systems (aka “network”): 1000s of interacting hardware/software components
other complex systems requiring monitoring, configuration, control:
  jet airplane, nuclear power plant, others?
NOC
Network Operations Centre
"Network management includes the deployment, integration
and coordination of the hardware, software, and human
elements to monitor, test, poll, configure, analyze, evaluate,
and control the network and element resources to meet the
real-time, operational performance, and Quality of Service
requirements at a reasonable cost."

## Slide 31: Components of network management
managed device
managed device
managed device
managed device
managed device
agent
data
agent
data
agent
data
agent
data
agent
data
managing
server/controller
data
Managing server: application, typically with network
managers (humans) in the loop
Managed device: equipment with manageable, configurable hardware, software components
Data: device “state” configuration data, operational data, device statistics
Network management protocol: used by managing server to query, configure, manage device; used by devices to inform managing server of data, events.

## Slide 32: SNMP protocol
managed device
agent
data
managing
server/controller
data
request
response
trap message
Two ways to convey MIB info, commands:
request/response mode
managed device
agent
data
managing
server/controller
data
trap mode
Event:
device fault

## Slide 33: SNMP protocol: message types
GetRequest
GetNextRequest
GetBulkRequest
manager-to-agent: “get me data”
(data instance, next data in list,
block of data).
Message type
Function
SetRequest
manager-to-agent: set MIB value
Response
Agent-to-manager: value, response to Request
Trap
Agent-to-manager: inform manager
of exceptional event

## Slide 34: Network layer: Summary
approaches to network control plane
  per-router control (traditional)
  logically centralized control (software defined networking)
traditional routing algorithms
  implementation in Internet: OSPF , BGP
SDN controllers
  implementation in practice: ODL, ONOS
Internet Control Message Protocol
network management
next stop: link layer!

## Slide 35: Assignment3, Lab
Assignment3:
due today! No late submission accepted
Lab:
build a Switch Router Network - related to Project2 (to be assessed in week12 lab)

## Slide 36: Lecture done
  ✅
Q&A