## Slide 1
Chapter 2 Application Layer
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Computer Networking: A Top-Down Approach 8th Edition, Global Edition Jim Kurose, Keith Ross Copyright © 2022 Pearson Education Ltd
Adapted by renping.liu@uts.edu.au on 4 March 2022
Notes: Version History
8.0 (April 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout

## Slide 2: Application layer: overview
2.1 Principles of network applications
2.2 Web and HTTP
2.3 E-mail, SMTP, IMAP
2.4 The Domain Name System DNS
2.5 P2P applications
2.6 video streaming and content distribution networks
2.7 socket programming with UDP and TCP

## Slide 3: Some network apps
social networking
Web
text messaging
e-mail
multi-user network games
streaming stored video (YouTube, Hulu, Netflix)
P2P file sharing
voice over IP (e.g., Skype)
real-time video conferencing (e.g., Zoom)
Internet search (google)
remote login
…
Q: your favorites?

## Slide 4: Creating a network app
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
write programs that:
run on (different) end systems
communicate over network
e.g., web server software communicates with browser software
no need to write software for network-core devices
network-core devices do not run user applications
applications on end systems allows for rapid app development, propagation

## Slide 5: Client-server paradigm
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
server:
always-on host
permanent IP address
often in data centers, for scaling
clients:
contact, communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
examples: HTTP, IMAP, FTP

## Slide 6: Peer-peer architecture
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
  self scalability – new peers bring new service capacity, as well as new service demands
peers are intermittently connected and change IP addresses
  complex management
example: P2P file sharing

## Slide 7: Processes communicating
process: program running within a host
within same host, two processes communicate using inter-process communication (defined by OS)
processes in different hosts communicate by exchanging messages
client process: process that initiates communication
server process: process that waits to be contacted
note: applications with P2P architectures have client processes & server processes
clients, servers
transport
application
physical
link
network
process
process
process

## Slide 8: Sockets
process sends/receives messages to/from its socket
socket analogous to mailbox door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door to deliver message to socket at receiving process
  two sockets involved: one on each side
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket
Socket: where a process plug into the network

## Slide 9: Addressing processes
to receive messages, process must have identifier
host device has unique 32-bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
identifier includes both IP address and port numbers associated with process on host.
example port numbers:
  HTTP server: 80
  mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
  IP address: 128.119.245.12
  port number: 80
more shortly…
  A: no, many processes can be running on same host
for network to identify a process

## Slide 10: An application-layer protocol defines:
types of messages exchanged,
  e.g., request, response
message syntax:
  what fields in messages & how fields are delineated
message semantics
  meaning of information in fields
rules for when and how processes send & respond to messages
open protocols:
defined in RFCs, everyone has access to protocol definition
allows for interoperability
e.g., HTTP, SMTP
proprietary protocols:
e.g., Zoom, MS Teams

## Slide 11: What transport service does an app need?
data integrity
some apps (e.g., file transfer, web transactions) require 100% reliable data transfer
other apps (e.g., audio) can tolerate some loss
timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
throughput
some apps (e.g., multimedia) require minimum amount of throughput to be “effective”
other apps (“elastic apps”) make use of whatever throughput they get
think of services by Aust Post: letter, registered, express, parcel,

## Slide 12: Transport service requirements: common apps
application
file transfer/download
e-mail
Web documents
real-time audio/video
streaming audio/video
interactive games
text messaging
data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
throughput
elastic
elastic
elastic
audio: 5Kbps-1Mbps
video:10Kbps-5Mbps
same as above
Kbps+
elastic
time sensitive?
no
no
no
yes, 10’s msec
yes, few secs
yes, 10’s msec
yes and no

## Slide 13: Internet transport protocols services
TCP service:
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum throughput guarantee, security
connection-oriented: setup required between client and server processes
UDP service:
unreliable data transfer between sending and receiving process
does not provide: reliability, flow control, congestion control, timing, throughput guarantee, security, or connection setup.
Q: why bother? Why is there a UDP?

## Slide 14: Internet transport protocols services
application
file transfer/download
e-mail
Web documents
Internet telephony
streaming audio/video
interactive games
application
layer protocol
FTP [RFC 959]
SMTP [RFC 5321]
HTTP 1.1 [RFC 7320]
SIP [RFC 3261], RTP [RFC 3550], or proprietary HTTP [RFC 7320], DASH
WOW, FPS (proprietary)
transport protocol
TCP
TCP
TCP
TCP or UDP
TCP
UDP or TCP

## Slide 15: Mid-break
  ☕️
Q&A

## Slide 16: Application layer: overview
2.1 Principles of network applications
2.2 Web and HTTP
2.3 E-mail, SMTP, IMAP
2.4 The Domain Name System DNS
2.5 P2P applications
2.6 video streaming and content distribution networks
2.7 socket programming with UDP and TCP

## Slide 17: Web and HTTP
First, a quick review…
web page consists of objects, each of which can be stored on different Web servers
object can be HTML file, JPEG image, Java applet, audio file,…
web page consists of base HTML-file which includes several referenced objects, each addressable by a URL, e.g.,
www.someschool.edu/someDept/pic.gif
host name
path name

## Slide 18: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model:
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
PC running
Firefox browser
server running
Apache Web
server
iPhone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 19: HTTP overview (continued)
HTTP uses TCP:
client initiates TCP connection (creates socket) to server, port 80
server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
server maintains no information about past client requests
protocols that maintain “state” are complex!
past history (state) must be maintained
if server/client crashes, their views of “state” may be inconsistent, must be reconciled
aside

## Slide 20: HTTP connections: two types
Non-persistent HTTP
at most one object sent over TCP connection
  TCP connection closed
downloading multiple objects required multiple connections
Persistent HTTP
multiple objects can be sent over single TCP connection between client, and that server

## Slide 21: Persistent HTTP (default)
User enters URL:
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80 “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(containing text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index

## Slide 22: Persistent HTTP (cont.)
User enters URL:
(containing text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index
4. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects Sends request for the 10 objects
5. HTTP server transmit 10 jpeg objects in the same TCP connection in one go!
time
6. HTTP client receives 10 jpeg
1 - 10 jpeg
…
…

## Slide 23: Persistent HTTP response time
persistent HTTP:
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects
Total response time
  2RTTs + Tx(html file)+ RTT+Tx(obj1)+Tx(obj2)+…)
time to
transmit
file
initiate TCP connection
RTT
request html file
time
time
RTT
html file received request all objects
receive all object
10 back-to-back requests
10 back-to-back objects
RTT

## Slide 24: Non-persistent HTTP: example
User enters URL:
1a. HTTP client initiates TCP connection to HTTP server (process) at www.someSchool.edu on port 80
2. HTTP client sends HTTP request message (containing URL) into TCP connection socket. Message indicates that client wants object someDepartment/home.index
1b. HTTP server at host www.someSchool.edu waiting for TCP connection at port 80 “accepts” connection, notifying client
3. HTTP server receives request message, forms response message containing requested object, and sends message into its socket
time
(containing text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index

## Slide 25: Non-persistent HTTP: example (cont.)
User enters URL:
(containing text, references to 10 jpeg images)
www.someSchool.edu/someDepartment/home.index
5. HTTP client receives response message containing html file, displays html. Parsing html file, finds 10 referenced jpeg objects
6. Steps 1-5 repeated for each of 10 jpeg objects
4. HTTP server closes TCP connection.
time
reopen-close a new connection each time for each object!

## Slide 26: Non-persistent HTTP: response time
RTT (definition): time for a small packet to travel from client to server and back
HTTP response time:
2xRTT for html file
  one RTT to initiate TCP connection
  one RTT for HTTP file
  Total: 2RTT+file transmission time
Object #1, 2…
  one RTT to initiate TCP connection
  one RTT for object file
  Total: 2RTT+file Tx time per object
Total response time
  2RTT+Tx(html file)+ 2RTT+Tx(object1)+ 2RTT+Tx(object2)+ 2RTT+Tx(object3)+ …
time to
transmit
file
initiate TCP connection
RTT
request html file
time
time
RTT
html file received
request object #1
request object #2
request object #3

## Slide 27: Persistent HTTP vs. Non-persistent HTTP
Non-persistent HTTP issues:
requires 2 RTTs per object
OS overhead for each TCP connection
browsers often open multiple parallel TCP connections to fetch referenced objects in parallel
Persistent HTTP (HTTP1.1):
server leaves connection open after sending response
subsequent HTTP messages between same client/server sent over open connection
client sends requests as soon as it encounters a referenced object
as little as one RTT for all the referenced objects (cutting response time in half)

## Slide 28: Non-persistent HTTP with parallel connections
browsers often open parallel TCP connections to fetch referenced objects
Total transmission time:
  2RTT+Tx(html file)+ 2RTT+Tx(all-objects-in-parallel)
think of 10 huge files transferred in parallel
Note: there is a limitation of the number of parallel connections
  e.g. with 10 parallel connections
RTT
time
time
RTT
request object #1
request object #2
request object #3

## Slide 29: Use of parallel connections
Persistent HTTP:
One connection per session
Non-persistent HTTP with parallel connections

## Slide 30: HTTP request message
two types of HTTP messages: request, response
HTTP request message:
  ASCII (human-readable format)
request line (GET, POST,
HEAD commands)
header
lines
carriage return, line feed at start of line indicates end of header lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Firefox/3.6.10\r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Accept-Charset: ISO-8859-1,utf-8;q=0.7\r\n
Connection: close\r\n
\r\n
carriage return character
line-feed character
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
Connection: non-persistent
Watch this in Lab

## Slide 31: HTTP request message: general format
request
line
header
lines
body
method
sp
sp
cr
lf
version
URL
cr
lf
value
header field name
cr
lf
value
header field name
~
~
~
~
cr
lf
entity body
~
~
~
~

## Slide 32: Other HTTP request messages
POST method: (for sending data, e.g. user inputs, to server)
web page often includes form input
user input sent from client to server in entity body of HTTP POST request message
GET method (for getting data, e.g. web page, from server)
include user data in URL field of HTTP GET request message (following a ‘?’):
www.somesite.com/animalsearch?monkeys&banana

## Slide 33: HTTP response message
status line (protocol
status code status phrase)
header
lines
data, e.g., requested
HTML file
HTTP/1.1 200 OK\r\n
Date: Sun, 26 Sep 2010 20:09:20 GMT\r\n
Server: Apache/2.0.52 (CentOS)\r\n
Last-Modified: Tue, 30 Oct 2007 17:00:02 GMT\r\n
ETag: "17dc6-a5c-bf716880"\r\n
Accept-Ranges: bytes\r\n
Content-Length: 2652\r\n
Connection: Keep-Alive\r\n
Keep-Alive: timeout=10, max=100\r\n
Content-Type: text/html; charset=ISO-8859-1\r\n
\r\n
data data data data data ...
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
Connection: persistent
timeout=10s,
max requests=100

## Slide 34: HTTP response status codes
200 OK
  request succeeded, requested object later in this message
301 Moved Permanently
  requested object moved, new location specified later in this message (in Location: field)
400 Bad Request
  request msg not understood by server
404 Not Found
  requested document not found on this server
505 HTTP Version Not Supported
status code appears in 1st line in server-to-client response message.
some sample codes:

## Slide 35: Trying out HTTP (client side) for yourself
1. Telnet to your favorite Web server:
opens TCP connection to port 80 (default HTTP server port) at gaia.cs.umass. edu.
anything typed in will be sent to port 80 at gaia.cs.umass.edu
telnet gaia.cs.umass.edu 80
3. look at response message sent by HTTP server!
(or use Wireshark to look at captured HTTP request/response)
2. type in a GET HTTP request:
GET /kurose_ross/interactive/index.php HTTP/1.1
Host: gaia.cs.umass.edu
by typing this in (hit carriage return twice), you send this minimal (but complete) GET request to HTTP server
Try this at home

## Slide 36: Maintaining user/server state: cookies
Recall: HTTP GET/response interaction is stateless
However, Susan access an e-commerce site from her PC
One week later, Susan returns to the site from the same PC
The site “remembers” what Susan did last time!
Cookies in Action:
when initial HTTP requests arrives at site, site creates:
  unique ID
  entry in backend database for ID
  All actions ”recorded” associating with the ID
when Susan returns:
  She is identified by the unique ID
  Her actions are recalled
Notes: t’

## Slide 37: Maintaining user/server state: cookies
client
server
usual HTTP response msg
usual HTTP response msg
cookie file
one week later:
usual HTTP request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual HTTP request msg
Amazon server
creates ID
1678 for user
create
entry
usual HTTP response
set-cookie: 1678
ebay 8734
amazon 1678
usual HTTP request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
amazon 1678
backend
database
time
time
Notes: t’

## Slide 38: HTTP cookies: comments
What cookies can be used for:
authorization
shopping carts
recommendations
user session state (Web e-mail)
cookies and privacy:
cookies permit sites to learn a lot about you on their site.
third party persistent cookies (tracking cookies) allow common identity (cookie value) to be tracked across multiple web sites
aside
Challenge: How to keep state:
protocol endpoints: maintain state at sender/receiver over multiple transactions
cookies: HTTP messages carry state
Notes: t’

## Slide 39: Web caches (proxy servers)
user configures browser to point to a Web cache
browser sends all HTTP requests to cache
  if object in cache: cache returns object to client
  else cache requests object from origin server, caches received object, then returns object to client
Goal: satisfy client request without involving origin server
client
proxy
server
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
origin
server
HTTP response
HTTP response
Notes: t’

## Slide 40: Web caches (proxy servers)
Web cache acts as both client and server
  server for original requesting client
  client to origin server
typically cache is installed by ISP (university, company, residential ISP)
Why Web caching?
reduce response time for client request
  cache is closer to client
reduce traffic on an institution’s access link
Internet is dense with caches
  enables “poor” content providers to more effectively deliver content
Notes: re: poor content providers – like in real-estate, location is everything. servers want to be close to clients.

## Slide 41: Chapter 2: Summary
Most importantly: learned about protocols!
typical request/reply message exchange:
  client requests info or service
  server responds with data, status code
message formats:
  headers: fields giving info about data
  data: info(payload) being communicated
important themes:
centralized vs. decentralized
stateless vs. stateful
scalability
reliable vs. unreliable message transfer
“complexity at network edge”

## Slide 42
Introductory Video:
  https://www.youtube.com/watch?v=UjiM4OTxpDg
    Led by past high-achieving students
    Share their learning tips in group study sessions
    Deeper understanding of subject materials
Starting from Week3!
  * Register in myTimetable

## Slide 43: Lecture done
  ✅
Q&A