## Slide 1
Computer Networking: A Top-Down Approach 8th Edition, Global Edition Jim Kurose, Keith Ross Copyright © 2022 Pearson Education Ltd
Chapter 4 Network Layer: Data Plane
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Adapted by renping.liu@uts.edu.au on 2 April 2023
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
added new 8th edition material on middleboxes (and Internet arch), Net neutrality, buffering …
lighter header font

## Slide 2: Network layer: “data plane” roadmap
4.1 Network layer: overview
  data plane
  control plane
4.2 What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
4.3 IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
4.4 Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
4.5 Middleboxes

## Slide 3: Network-layer services and protocols
transport segment from sending to receiving host
  sender: encapsulates segments into datagrams, passes to link layer
  receiver: delivers segments to transport layer protocol
network layer protocols in every Internet device: hosts, routers
routers:
  examines header fields in all IP datagrams passing through it
  moves datagrams from input ports to output ports to transfer datagrams along end-end path
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 4: Two key network-layer functions
network-layer functions:
routing: determine route taken by packets from source to destination
  routing algorithms
forwarding: move packets from router’s input to appropriate router output
analogy: taking a trip
routing: process of planning trip from source to destination
forwarding: process of getting through single interchange
Trip: Forster  Orange

## Slide 5: Network layer: data plane, control plane
Data plane
determines how datagram arriving on router input port is forwarded to router output port
local, per-router function
Based on pre-determined forwarding
Control plane
determines how datagram is routed among routers along end-end path from source host to destination host
network-wide logic
Based on network topology
1
2
3
0111
values in arriving
packet header

## Slide 6: Network layer: data plane, control plane
Control plane
determines how datagram is routed among routers along end-end path from source host to destination host
network-wide logic
Based on network topology
Two control-plane approaches:
traditional routing algorithms: implemented in routers
software-defined networking (SDN): implemented in (remote) servers

## Slide 7: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3
0111 network
0111 4
0111 2

## Slide 8: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 9: Network service model
example services for individual datagrams:
guaranteed delivery
guaranteed timing, e.g., delivery within 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing
Q: What service model do we need for “network” to pass datagrams from sender to receiver?
think of services by Aust Post: letter, registered, express, parcel,

## Slide 10: Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model
Quality of Service (QoS) Guarantees ?

## Slide 11: Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
🚫QoS: too hard, too expensive!
Quality of Service (QoS) Guarantees ?

## Slide 12: Reflections on best-effort service:
simplicity of mechanism has allowed Internet to be widely deployed adopted
sufficient provisioning of bandwidth allows performance of real-time applications (e.g., interactive voice, video) to be “good enough” for “most of the time”
replicated, application-layer distributed services (datacenters, content distribution networks) connecting close to clients’ networks, allow services to be provided from multiple locations
congestion control of “elastic” services helps
It’s hard to argue with success of best-effort service model

## Slide 13: Network layer: “data plane” roadmap
4.1 Network layer: overview
  data plane
  control plane
4.2 What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
4.3 IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
4.4 Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
4.5 Middleboxes

## Slide 14: Router architecture overview
data plane (hardware)
Operates in ns timeframe
forwarding datagram
control plane (software)
operates in ms time frame
routing, management
Four parts:
  routing processor
  Input ports
  Switching fabrics
  Output ports
Hardware
Software
A specialised computer

## Slide 15: Input port functions
switch
fabric
line
termination
physical layer:
bit-level reception
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
input port queuing: if datagrams arrive faster than forwarding rate into switch fabric

## Slide 16: Input port functions
line
termination
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
switch
fabric
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)

## Slide 17: Input port queuing
If switch fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
output port contention: only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward

## Slide 18: Switching fabrics
transfer packet from input link to appropriate output link
high-speed
switching
fabric
N input ports
N output ports
. . .
. . .
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
R
R
R
R
(rate: NR, ideally)

## Slide 19: Switching fabrics
bus
memory
memory
interconnection
network
three major types of switching fabrics:
transfer packet from input link to appropriate output link
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable

## Slide 20: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 21: Switching via a bus
datagram from input port memory to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access routers

## Slide 22: Switching via interconnection network
Crossbar, Clos networks, other interconnection nets initially developed to connect processors in multiprocessor
8x8 multistage switch
built from smaller-sized switches
3x3 crossbar
multistage switch: nxn switch from multiple stages of smaller switches
exploiting parallelism:
  fragment datagram into fixed length cells on entry
  switch cells through the fabric, reassemble datagram at exit
3x3 crossbar

## Slide 23: Output port queuing
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!

## Slide 24: Output port queuing
Buffering required when datagrams arrive from fabric faster than link transmission rate.
Scheduling discipline chooses among queued datagrams for transmission
Datagrams can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R
Drop policy: which datagrams to drop if no free buffers?

## Slide 25: Packet Scheduling: FCFS
packet scheduling: deciding which packet to send next on link
  first come, first served
  priority
  round robin
  weighted fair queueing
FCFS: packets transmitted in order of arrival to output port
also known as: First-in-first-out (FIFO)
real world examples?
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R

## Slide 26: Scheduling policies: priority
Priority scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
high priority queue
low priority queue
arrivals
classify
departures
link
1
3
2
4
5
arrivals
departures
packet in service
send packet from highest priority queue that has buffered packets
  FCFS within priority class
1
3
4
2
5
1
3
2
4
5
Real life example:
Airline check-in

## Slide 27: Scheduling policies: round robin
Round Robin (RR) scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
classify
arrivals
departures
link
R
server cyclically, repeatedly scans class queues, sending one complete packet from each class (if available) in turn
Real life example:
RMS, Medicare, …
true round robin, or?

## Slide 28: Scheduling policies: weighted fair queueing
Weighted Fair Queuing (WFQ):
generalized Round Robin
classify
arrivals
departures
link
R
w1
w2
w3
wi
Sjwj
minimum bandwidth guarantee (per-traffic-class)
each class, i, has weight, wi, and gets weighted amount of service in each cycle:
Real life example:
RMS, Medicare, …
true round robin, or WFQ

## Slide 29: Buffer Management
buffer management:
drop: which packet to add, drop when buffers are full
  tail drop: drop arriving packet
  priority: drop/remove on priority basis
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
scheduling
marking: which packets to mark to signal congestion (ECN, RED)
R
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R

## Slide 30: Sidebar: Network Neutrality
What is network neutrality?
  technical: how an ISP should share/allocation its resources
  packet scheduling, buffer management are the mechanisms
  social, economic principles
    protecting free speech
    encouraging innovation, competition
  enforced legal rules and policies
Different countries have different “takes” on network neutrality
Optional – not tested

## Slide 31: Sidebar: Network Neutrality
2015 US FCC Order on Protecting and Promoting an Open Internet: three “clear, bright line” rules:
no blocking … “shall not block lawful content, applications, services, or non-harmful devices, subject to reasonable network management.”
no throttling … “shall not impair or degrade lawful Internet traffic on the basis of Internet content, application, or service, or use of a non-harmful device, subject to reasonable network management.”
no paid prioritization. … “shall not engage in paid prioritization”
Optional – not tested

## Slide 32: ISP: telecommunications or information service?
US Telecommunication Act of 1934 and 1996:
  Title II: imposes “common carrier duties” on telecommunications services: reasonable rates, non-discrimination and requires regulation
  Title I: applies to information services:
    no common carrier duties (not regulated)
    but grants FCC authority “… as may be necessary in the execution of its functions”4
Is an ISP a “telecommunications service” or an “information service” provider?
the answer really matters from a regulatory standpoint!
Optional – not tested

## Slide 33: Mid-break
  ☕️
Q&A

## Slide 34: Network layer: “data plane” roadmap
4.1 Network layer: overview
  data plane
  control plane
4.2 What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
4.3 IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
4.4 Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
4.5 Middleboxes

## Slide 35: Network Layer: Internet
host, router network layer functions:
IP protocol
datagram format
addressing
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer
forwarding
table
Path-selection algorithms: implemented in
routing protocols (OSPF, BGP)
SDN controller

## Slide 36: IP Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 37: IP Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
20 bytes
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead for TCP+IP
overhead

## Slide 38: IP Datagram format - TTL
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
TTL: remaining max hops
(decremented at each router)
Purpose: get rid of looping datagram
Router process:
  TTL -= 1
  if TTL == 0: drop(datagram)
TTL

## Slide 39: TTL and Traceroute
source sends series of UDP segments to destination
  1st set has TTL =1, discarded at 1st router  notify source, source record router and round-trip time.
  2nd set has TTL=2, discarded at 2nd router  notify source, source record router and round-trip time.
  ...
  reach destination with unlikely port number: destination host notify source with “port unreachable”, source record destination and round-trip time.
Source now has
  A list of all routers and their round-trip time along the path
  the destination and destination round-trip time.
3 probes
3 probes
3 probes
This week’s Lab

## Slide 40: Network layer: “data plane” roadmap
4.1 Network layer: overview
  data plane
  control plane
4.2 What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
4.3 IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
4.4 Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
4.5 Middleboxes

## Slide 41: IP address: introduction
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
    only one interface is active at a time
223.1.10.5
223.1.1.4
223.1.2.9
223.1.3.27
223.1.10.5 = 11011111 00000001 00001010 00000101
223
1
5
10
One IP address for each interface

## Slide 42: IP address: decimal  binary
223.1.10.5 = 11011111.01100100.00001010.00000101
223
100
5
10
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
2. convert 10 to binary: 10-8=2; 2-2=0. (deduct numbers: high to low)
100 - 64 = 36; 36 - 32 = 4; 4 - 4 = 0
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
2. converting 100 to binary: deduct numbers: high to low
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  | i
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  | 2i
1. Write down binary table:
Try 223?
3.
3.

## Slide 43: IP address: binary decimal
2. write binary byte under the table:
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |  | i
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  | 2i
1. Write down binary table:
64 + 32 + 4 = 100
3. add 1’s values:
223.1.10.5 = 11011111.01100100.00001010.00000101
223
100
5
10

## Slide 44: IP addressing: introduction
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Q: how are interfaces actually connected?
A: wired
Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
A: we’ll learn about that in chapters 6, 7
subnet
subnet
subnet
subnet

## Slide 45: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
  Analogy: Houses in a Street
IP addresses have structure:
  subnet part: common high order bits
  host part: low order bits
IP address: subnet.host# 223.1.1.3
Street addr: street.house# Smith St.3
network consisting of 3 subnets
3 Smith St

## Slide 46: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Recipe for defining subnets:
group IP addresses with the same high order part
creating “islands” of isolated networks
each isolated network is called a subnet
subnet mask: /24
(high-order 24 bits: subnet part of IP address)
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24
Write IP address
  IP address: 223.1.1.3 subnet mask: 255.255.255.0
  shorthand: 223.1.1.3/24

## Slide 47: Subnets
where are the subnets?
  how many subnets?
what are the subnet addresses?
  223.1.1.0/24
  ...
  223.1.9.0/24
host IP address?
router IP address?
  router: gateway to outside
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1.0/24
subnet 223.1.7.0/24
subnet 223.1.3.0/24
subnet 223.1.2.0/24
subnet 223.1.9.0/24
subnet 223.1.8.0/24

## Slide 48: IP Address - Classful
Class | Start Address | End Address | Subnet Mask | shorthand
A | 0.0.0.0 | 127.255.255.255 | 255.0.0.0 | /8
B | 128.0.0.0 | 191.255.255.255 | 255.255.0.0 | /16
C | 192.0.0.0 | 223.255.255.255 | 255.255.255.0 | /24

## Slide 49: IP addressing: CIDR
CIDR: Classless InterDomain Routing (pronounced “cider”)
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 50: Chapter 4 – part1: Summary
Question: how are forwarding tables (destination-based forwarding) or flow tables (generalized forwarding) computed?
Answer: by the control plane (next chapter)
Forwarding/routing
Middleboxes
Network layer: overview
What’s inside a router
IP addressing, subnet

## Slide 51: Good Friday
Friday tut/lab moved to the following week – your tutor will let you know.

## Slide 52: Lecture done
  ✅
Q&A