## Slide 1
Computer Networking: A Top-Down Approach 8th Edition, Global Edition Jim Kurose, Keith Ross Copyright © 2022 Pearson Education Ltd
Chapter 4 Network Layer: Data Plane
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Adapted by renping.liu@uts.edu.au on 17 April 2023
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
added new 8th edition material on middleboxes (and Internet arch), Net neutrality, buffering …
lighter header font

## Slide 2: Network layer: “data plane” roadmap
4.1 Network layer: overview
  data plane
  control plane
4.2 What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
4.3 IP: the Internet Protocol
  datagram format
  addressing
  network address translation
  IPv6
4.4 Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
4.5 Middleboxes

## Slide 3: IP addresses: how to get one?
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)

## Slide 4: IP addresses: how to get one?
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Manually config by sysadmin in config file
  Windows: control-panelnetworkconfigurationTCP/IP
  Apple: system preferencesnetworksadvanced TCP/IP
DHCP: Dynamic Host Configuration Protocol:
  dynamically get address from as server
  “plug-and-play”

## Slide 5: DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg

## Slide 6: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
DHCP server
223.1.2.5
arriving DHCP client needs
address in this network
Typically, DHCP server will be co-located in router, serving all subnets to which router is attached

## Slide 7: DHCP client-server scenario
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Broadcast: OK. You’ve got that IP address!
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]

## Slide 8: DHCP: example
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demux’ed to IP demux’ed, UDP demux’ed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 9: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulated DHCP server reply forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router

## Slide 10: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  network mask
    indicating network versus host portion of address
    so given a dest IP address, I know if it is in my local area network or outside
  address of first-hop router for client
    to access the wide Internet
  name and IP address of DNS sever
    to resolve www.amazon.com.au into 13.224.170.88

## Slide 11: IP addresses: how to get one?
That’s actually two questions:
Q: How does a host get IP address within its network (host part of address)?
Q: How does a network get IP address for itself (network part of address)
A: gets allocated from its provider ISP’s address space
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned Names and Numbers http://www.icann.org/
  allocates IP addresses, through 5 regional registries (RRs)

## Slide 12: IP routing: forwarding
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Internet
203.5.121.6
Forwarding in a Host
Forwarding in a Router
  Forwarding table
  Aggregation
  Longest match

## Slide 13: IP routing: forwarding in a Host
Configure host IP address:
Forwarding a datagram:
  subnet = (IP address) AND (subnet mask)
  if src.subnet == dest.subnet (dest: 223.1.1.3) send directly to current subnet – layer2, no routing.
  if src.subnet != dest.subnet (dest: 223.1.3.2) go via router (223.1.1.4)
  Router to do further routing …
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Internet
203.5.121.6
IP address: 223.1.1.2
Subnet mask: 255.255.255.0
Router: 223.1.1.4

## Slide 14: IP Routing: forwarding table in a router
200.23.1.0/24
200.23.2.0/24
200.23.7.0/24
Team 1
Team 7
Internet
Team 2
ISPs-R-Us
200.23.3.0/24
Team 3
.
.
.
.
.
.
Forwarding Table: match IP network address to outgoing interface
int0
int1
int2
int7
Dest Addr Range | Int
200.23.1.0/24 | 0
200.23.2.0/24 | 1
200.23.3.0/24 | 2
… | …
200.23.7.0/24 | 7
otherwise | 15
int0
int1
int15
incoming IP datagram:
Dest: 200.23.2.5
Destination-based Forwarding
Get dest.subnet
Match forwarding table entry?
  Yes: forward to int# – done.
  No: try next entry – loop…
No match (otherwise)  default interface

## Slide 15: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.0.0/16”
200.23.1.0/24
200.23.2.0/24
200.23.7.0/24
Team 1
Team 7
Internet
Team 2
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.3.0/24
Team 3
.
.
.
.
.
.
int0
int1
int2
int7
Dest Addr Range | Int
200.23.0.0/16 | 0
199.31.0.0/16 | 1
… | …
int0
int1
hierarchical addressing allows efficient advertisement of routing
information:
Dest Addr Range | Int
200.23.1.0/24 | 0
200.23.2.0/24 | 1
… | …
200.23.7.0/24 | 7
otherwise | 15
int15
199.31.1.0/24
.
.
.
incoming IP datagram:
int0  200.23.2.5
int1  199.31.1.8

## Slide 16: Longest prefix matching
“Send me anything
with addresses
beginning
200.23.0.0/16”
200.23.1.0/24
200.23.2.0/24
200.23.7.0/24
Team 1
Team 7
Internet
Team 2
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16
or 200.23.5.0/24”
200.23.4.0/24
Team 3
.
.
.
.
.
.
int0
int1
int2
int7
Dest Addr Range | Int
199.31.0.0/16 | 1
200.23.0.0/16 | 0
200.23.5.0/24 | 1
… | …
int0
int1
ISPs-R-Us has a more specific route to Team 18
200.23.5.0/24
Team 5
when looking for forwarding table entry for given destination address,
use longest address prefix that matches destination address.
Dest Addr Range | Int
200.23.1.0/24 | 0
200.23.2.0/24 | 1
… | …
200.23.34.0/24 | 7
otherwise | 15
int15
incoming IP datagram:
200.23.5.2
199.31.1.0/24
.
.
.

## Slide 17: IP addressing: last words ...
Q: are there enough 32-bit IP addresses?
ICANN allocated last chunk of IPv4 addresses to RRs in 2011
NAT (next) helps IPv4 address space exhaustion
IPv6 has 128-bit address space
"Who the hell knew how much address space we needed?" Vint Cerf (reflecting on decision to make IPv4 address 32 bits long)

## Slide 18: Mid-break
  ☕️
Q&A

## Slide 19: Network layer: “data plane” roadmap
4.1 Network layer: overview
  data plane
  control plane
4.2 What’s inside a router
  input ports, switching, output ports
  buffer management, scheduling
4.3 IP: the Internet Protocol
  datagram format
  addressing
  network address translation (NAT)
  IPv6
4.4 Generalized Forwarding, SDN
  Match+action
  OpenFlow: match+action in action
4.5 Middleboxes

## Slide 20: NAT: network address translation
192.168.1.1
192.168.1.2
192.168.1.4
138.76.29.7
local network
(e.g., campus, home network)
private IP address:
192.168.1.0/24
Internet
public IP address:
138.76.29.7
192.168.1.3
Private IP: free, reuse!
Cannot go to public Internet
Class | Private IP address range | Subnet mask
A | 10.0.0.0 - 10.255.255.255 | 255.0.0.0
B | 172.16.0.0 - 172.16.31.255 | 255.255.0.0
C | 192.168.0.0-192.168.255.255 | 255.255.255.0
NAT: all devices in local network share just one public IPv4 address as far as outside world is concerned
Private IP Address

## Slide 21: NAT: network address translation
  all devices in local network have “private” IP addresses
    10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16 prefixes
    can only be used in local network, discarded in public routers
  advantages:
    just one IP address needed from provider ISP for all devices
    can change addresses of host in local network without notifying outside world
    can change ISP without changing addresses of devices in local network
    security: devices inside local net not directly addressable, invisible to outside world

## Slide 22: NAT: network address translation
192.168.1.1
192.168.1.2
192.168.1.3
192.168.1.4
local network (e.g., home network) 192.168.1/24
138.76.29.7
rest of
Internet
datagrams with source or destination in this network have 192.168.1/24 address for source, destination (as usual)
all datagrams leaving local network have same source NAT IP address: 138.76.29.7, but different source port numbers
NAT: all devices in local network share just one IPv4 address as far as outside world is concerned

## Slide 23: NAT: network address translation
implementation: NAT router must (transparently):
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
      remote clients/servers will respond using (NAT IP address, new port #) as destination address
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 24: NAT: network address translation
192.168.1.1
192.168.1.2
192.168.1.3
S: 192.168.1.1, 3345
D: 128.119.40.186, 80
1
192.168.1.4
138.76.29.7
1: host 192.168.1.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 192.168.1.1, 3345
…… ……
S: 128.119.40.186, 80
D: 192.168.1.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
192.168.1.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 192.168.1.1, 3345
128.119.40.186

## Slide 25: NAT: network address translation
192.168.1.1
192.168.1.2
192.168.1.3
S: 192.168.1.1, 3345
D: 128.119.40.186, 80
1
192.168.1.4
138.76.29.7
1: host 192.168.1.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 192.168.1.1, 3345
…… ……
S: 128.119.40.186, 80
D: 192.168.1.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
192.168.1.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 192.168.1.1, 3345
128.119.40.186
This week’s Lab

## Slide 26: NAT: network address translation
NAT has been controversial:
  routers “should” only process up to layer 3
  address “shortage” should be solved by IPv6
  violates end-to-end argument (port # manipulation by network-layer device)
  NAT traversal: what if client wants to connect to server behind NAT?
but NAT is here to stay:
  extensively used in home and institutional nets, 4G/5G cellular nets

## Slide 27: IPv6: motivation
initial motivation: 32-bit IPv4 address space would be completely allocated
additional motivation:
  speed processing/forwarding: 40-byte fixed length header
  enable different network-layer treatment of “flows”

## Slide 28: IPv6 datagram format
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
priority: identify priority among datagrams in flow
flow label: identify datagrams in same "flow.” (concept of “flow” not well defined).
128-bit
IPv6 addresses
What’s missing (compared with IPv4):
no checksum (to speed processing at routers)
no fragmentation/reassembly
no options (available as upper-layer, next-header protocol at router)
40 Bytes

## Slide 29: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers (“packet within a packet”)
  tunneling used extensively in other contexts (4G/5G)

## Slide 30: Tunneling and encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
IPv4 network
IPv4 network connecting two IPv6 routers

## Slide 31: Tunneling and encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
IPv4 tunnel connecting two IPv6 routers
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
E
F
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
IPv4 datagram
IPv6 datagram
tunneling: IPv6 datagram as payload in a IPv4 datagram
IPv6/v4
IPv6/v4

## Slide 32: Tunneling
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
IPv4
IPv4
E
IPv6/v4
IPv6
F
C
D
A
B
IPv6
IPv6/v4
logical view:
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
Note source and destination addresses!

## Slide 33: IPv6: adoption
Google1: ~ 30% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
1 https://www.google.com/intl/en/ipv6/statistics.html

## Slide 34: IPv6: adoption
Google1: ~ 30% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment and use
  25 years and counting!
  think of application-level changes in last 25 years: WWW, social media, streaming media, gaming, telepresence, …
  Why?
1 https://www.google.com/intl/en/ipv6/statistics.html

## Slide 35: Chapter 4: done!
Question: Where do we get the forwarding tables?
Answer: by the control plane (next chapter)
Generalized Forwarding, SDN
Middleboxes
Network layer: overview
What’s inside a router
IP: the Internet Protocol

## Slide 36: Exam info (tentative)
Date,Time: 05/06/2023, 9:30am,
Duration: 120min
Format: online open book
Scope: weeks 5-12

## Slide 37: Lecture done
  ✅
Q&A